## Slide 1: Scalable BLE Cluster Fingerprinting for High-Density IoT Environments
Johanna Bieri
Master Thesis: Midterm Presentation
Supervisor: Katharina Müller

## Slide 2: Content
Thesis Motivation
Technical Background
Thesis Goals
Preceding Master Thesis (Joel Meier, 2025): Approach & Results
My Approach
Next Steps
Q&A

## Slide 3: Thesis Motivation
Bluetooth devices are ubiquitous
Bluetooth Low Energy (BLE)
  Used for device discovery and connection initiation
  Transmitted over public channels  Significant privacy concerns
 Generalizability: Can we reliably identify device cluster of different ecosystems?
 Scalability: What happens if we have two or more groups consisting of the same devices?
Image generated by GPT-5
1 - Thesis Motivation
Heinrich et al., 2022, AirGuard- Protecting Android Users From Stalking Attacks By Apple Find My Devices

## Slide 4: BLE Introduction
Bluetooth Low Energy
Low energy consumption due to:
  Low data rate
  Small packet size
BLE operates on 40 channels
  3 primary advertising channels: 37, 38, 39
  37 secondary advertising channels
Image from NordicSemi
https://sp-ao.shortpixel.ai/client/to_webp,q_glossy,ret_img,w_1201/https://academy.nordicsemi.com/wp-content/uploads/2023/03/blefund_less1_ad_channels.png
2 - Technical Background

## Slide 5: Bluetooth LE Advertisement Packet Structure
Image from NordicSemi
https://academy.nordicsemi.com/courses/bluetooth-low-energy-fundamentals/lessons/lesson-2-bluetooth-le-advertising/topic/advertisement-packet/
2 - Technical Background

## Slide 6: Dataset Generation
Laptop as capturing device:
  nRF Sniffer attached via USB
  Wireshark and BLE plugin running
BLE devices:
  Target device group (same ecosystem within group)
  Connected via Bluetooth
Data extraction:
  Select relevant columns (based on preceding thesis)
  Extract as .csv from Wireshark
Image from NordicSemi
https://academy.nordicsemi.com/courses/bluetooth-low-energy-fundamentals/lessons/lesson-6-bluetooth-le-sniffer/topic/nrf-sniffer-for-bluetooth-le/
Wireshark
Sniffer
2 - Technical Background

## Slide 7: Wireshark Example Data
Image of Wireshark UI
2 - Technical Background

## Slide 8: Fingerprinting
Unique characteristics in a device’s communication behavior
  Here: fingerprint of group when connected
Can be done for different kinds of network traffic
  Here: for BLE
 Use to train ML models
Image generated by GPT-5
2 - Technical Background

## Slide 9: Thesis Goals
Generate datasets for groups of connected BLE devices (recorded together)
  For different ecosystems
Create a fingerprint of that device group and evaluate it on pre-trained models
Retrain models to improve performance on new datasets
Evaluate the models in high-density environments to test their robustness
Image generated by GPT-5
3 - Thesis Goals

## Slide 10: Preceding Master Thesis by Joel Meier (2025) - Approach
Trained ML models for a target group consisting of three Samsung devices (smartphone, earphones, smart tag)
  Supervised modeling: Random Forest, Multi-Layer Perceptron, Stochastic Gradient Descent
  Unsupervised modeling: Kmeans, BisectingKMeans, Birch
Demonstrated that models can identify the device cluster even in noisy environments
Baseline work for my thesis
4 - Preceding MT Joel Meier

## Slide 11: Preceding Master Thesis by Joel Meier (2025) - Results
Joel’s model selection:
  Supervised Modeling
    Random Forest
    Multi-Layer Perceptron
    Stochastic Gradient Descent
    Trained on medium density dataset (recorded in apartment)
  Unsupervised Modeling (cluster algorithms)
    KMeans (bottom-up)
    BisectingKMeans (top-down)
    Birch
4 - Preceding MT Joel Meier

## Slide 12: Results MT Joel Meier Supervised Models
4 - Preceding MT Joel Meier

## Slide 13: Results MT Joel Meier Unsupervised Models
4 - Preceding MT Joel Meier

## Slide 14: My Approach
Feasibility Testing
Generate new datasets
  Samsung setup: Galaxy S22 smartphone, Smart Tag, (Galaxy Buds FE)
  Apple setup: iPad, AirPods Pro, AirTag
  Different density: Isolated (basement), Medium-density (apartment), High-density (uni)
Evaluate isolated datasets with existing models (no retraining)
Hypotheses:
  Models will show limited performance on Samsung dataset, same ecosystem but different devices and device number
  Models will perform poorly on Apple dataset, because trained with Samsung devices only
Based on the first results: either focus on generalizability or scalability first
5 - My Approach

## Slide 15: Results MT Joel Meier - High-Density Dataset (Uni) Supervised Models
5 - My Approach

## Slide 16: Evaluation Samsung Setup without Interference (Basement) Supervised Models
5 - My Approach

## Slide 17: Evaluation Samsung Setup with Medium Interference (Apartment) Supervised Models
5 - My Approach

## Slide 18: Evaluation Apple Setup without Interference (Basement) Supervised Models
5 - My Approach

## Slide 19: Bonus - Interesting Observation with Apple Group
5 - My Approach

## Slide 20: Next Steps
Investigate importance of number of devices:
  Joel’s target group consisted of 3 devices  current Samsung setup has 2
  Generate a new Samsung dataset with 3 devices: phone, smart tag, and buds
  Evaluate with existing model
Generalizability:
  Train new models to only perform well for Apple ecosystem or retrain existing models to also perform well for clusters consisting of Apple devices
  Retrain existing models to work for clusters of mixed ecosystems
Scalability:
  Record two identical setups at the same time
  Evaluate with pre-trained models, retrain if necessary
6 - Next Steps

## Slide 21: Thank you for your attention. Questions and feedback are welcome.
7 - Q&A